## Slide 1
Notes: Title — ~1 min. Two big ideas today: reading analog sensors, and doing two things at once. Site: https://aicodeacademy.com

## Slide 2
Notes: Introduction — quick verbal check before moving on: 'what does the # do in a command string?' Reuse the setup -> work -> destroy framing from Lessons 1 and 2.

## Slide 3
Notes: Goals — emphasise 'at the same time'. That's the new concept, not just reading sensors. Show the finished demo once if you can so they know the target.

## Slide 4
Notes: What is an ADC — analogy: a dimmer switch (smooth) vs a light switch (on/off). The ADC reads the dimmer's position as a number. adc.recvADC(channel) returns volts.

## Slide 5
Notes: The sensors — have students physically find the two little light sensors (photoresistors) on their board. 'Read a sensor' = 'read its channel number'. Asset to source: close-up photo of the two photoresistors.

## Slide 6
Notes: Battery math — the ADC sees one third of the pack voltage, so multiply by 3. Tie to real life: phones do the same voltage -> percent estimate.

## Slide 7
Notes: What is multithreading — analogy: cooking dinner (main thread) while a timer watches the oven (background thread). Both happen at once. Asset to source: a simple two-threads-side-by-side diagram.

## Slide 8
Notes: Threads, daemons & the stop flag — keep it light. 'daemon = quits with the program' and 'Event = a stop switch' is enough. Don't go deep on OS theory.

## Slide 9
Notes: Imports (chunk 1) — point out that Thread and Event are standard Python, not car-specific. car_setup must be imported first.

## Slide 10
Notes: ADC channels (chunk 2) — naming the channels instead of bare 0/1/2 is a good-code habit worth praising.

## Slide 11
Notes: Battery thresholds (chunk 3) — these are the numbers students will tweak on the 'try it yourself' slide.

## Slide 12
Notes: Empty boxes + the stop flag (chunk 4) — the flag exists BEFORE the thread that reads it. Order matters. Event() starts 'not set'; we call set() to stop.

## Slide 13
Notes: setup() starts the thread (chunk 5) — three steps for a thread: make it (Thread(...)), set daemon, start it. We write monitor_battery next.

## Slide 14
Notes: Reading & scaling the battery (chunk 6) — optional: ask what int(7.6 V) maps to (~42%) to check understanding. Remember the x3.

## Slide 15
Notes: beep() helper (chunk 7) — reuses the buzzer '1'/'0' string idea from Lesson 2 — quick callback. '_' is a throwaway counter.

## Slide 16
Notes: monitor_battery() (chunk 8) — 'while not stop_event.is_set()' is how the thread knows when to quit. Link it forward to destroy(). Beeps more the lower it gets.

## Slide 17
Notes: loop() the main thread (chunk 9) — now there are TWO while loops alive at once (this one + monitor_battery). That's multithreading in action.

## Slide 18
Notes: destroy() (chunk 10) — the payoff for the daemon/Event slide: set the flag, join(timeout=2) so we never hang, then i2cClose() to close the ADC.

## Slide 19
Notes: Main block (chunk 11) — third lesson in a row with this try / except / finally block. Students should recognise it instantly now.

## Slide 20
Notes: Whole file (chunk 12) — scroll the assembled file; highlight the TWO functions that loop (loop and monitor_battery).

## Slide 21
Notes: Run it — point at the mixed output: proof both threads run at once. Light prints every 1 s, battery every 3 s. Use sudo for consistency across the course. Ctrl+C to stop.

## Slide 22
Notes: Try it yourself — demo 'cover the sensor' early; it's the most tangible moment. The brighter-side challenge previews line-following / light-seeking logic.

## Slide 23
Notes: Troubleshooting — if I2C errors appear, check raspi-config (I2C enabled) and the ADC seating. Remember the battery x3. Give Ctrl+C a second to join the thread.

## Slide 24
Notes: Recap — celebrate: they've now touched every core subsystem of the car (lights, sound, motors, commands, sensors). Next: smarter, more autonomous behavior.

## Slide 25
Notes: COACH (hidden) — do not present. After class: post the recap, log absent students in the Discord #attendance channel. Before next class confirm I2C is enabled on each Pi and charge the cars.